Alpha Spec Sheet

J. Linnemann

March 9, 2001

Beta should meet or exceed specs (critical specs italicized), and provide this functionality

In cases where it can’t, need to explain how that’s dealt with

Occupies 2 slots; power: +12 2A: +5 20A; +3.3 10A; -5.2 1.25A; -12 1A;      total,   176W

Processing power 500 MHz 21164

2 integer, 2 floating pipes; 64 bits wide (used in bit searches and PIO)

96kB on-chip L2 cache; 3-way associative

enough cache for data for event

+ enough instructions for 24 μsec of non-looping execution

(L3 cache (4MB) does not work, doesn’t SEEM to be needed

because of characteristics of L2 cache above)

SI95	15	SF95   21

Executes L2 algorithms < 50μsec/event with new data each event

# Linux/RT Unix OS        (include licenses in costs)

- Association with physical memory (for buffers and device drivers)

- Possibility of direct memory mapping (possibly running in MMU-less mode) (?)

- Low overhead operating system (zero/low CPU use during running)

  - E.g. preemptive multitasking, with trigger code at (nearly) highest or priority

- Interrupt handler for DMA and SCL_INIT (source code?)

- Core dump files – need to load and examine core files at a later date

- Offline environment:

  - need code development workstation

  - must be able to run offline simulator on same platform for trigger verification

- Efficient modern C++ compiler:

  - Support for ANSI C++; especially namespaces and templates

  - Support for KAI compiler would be a big bonus!

- Data formats specified as little endian; 1 and 2-byte instructions

- (JTAG interface into CPU would be nice)

PCI devices:	 	VME, TSI, DMA, PIO

VME via Universe II		32 bit wide used

## 16MB/s for L3 readout

Geographic addressing for initialization

Programmable interrupts

16, 24, and 32 bit addressing modes for handling VME devices in crate

TSI:

J2 interface:  (TTL levels)

DØ minimum: 4 inputs, 6 outputs

IN:	2 inputs generate PCI interrupts

L2_Answer_Ready; VBD_DONE

OUT:	VBD_START; 5 “worker interrupt out”

CDF uses more; see web sites

Front panel interface:

DØ minimum	32 bit ECL Output register  (used for monitoring)

CDF: 			32 bit LVDS; bi-directional (split unknown)

Mbus DMA			80-100MB/s  ( at about 40% PCI occupancy)

Address translation for 10 bits of destination base address

16 events x 64 sources

reserved Mbus addresses 00yy	where yy is lower 10 bits; 00 is upper 22 bits = 0

64 KB input FIFO

DMA destination set up by CPU

Time to re-set destinations after an event ~ .2 μsec/source

Time for PCI startup of DMA: 5-8 X 30ns PCI cycles after PCI mastership

Mbus mastered by MBT

Broadcast across processors

Support for MBT control protocol

PCI Interrupt at end of full-event DMA (all sources)

for all boards in broadcast

AP_FIFO Empty logic

set DONE_OUT

read MOD_DONE register (20 bits or so)

set(Administrator) or read START_LOAD	Toggle Administrator/Worker

DMA may be turned off for debugging

Any other Mbus signals used:

Mbus PIO	16MB/s	1μsec latency  even during DMA

latency driven by CIA buffers filling: pauses every .3-.6 μsec in DMA

Note: 64 bit PCI means 16B Mbus PIO in 2 PCI cycles, not 4

2 modes: 1 MBus cycle ever 128 PIO bits (2 PIO cycles), one every PIO cycle (64 bit)

current firmware uses only 32-bit PCI cycles; to be upgraded

Mbus Arbitration in PECL, estimated < 15ns

Master/Write	to Mbus devices (32 bit address)

Worker Output to Global; Global Answer to L2HWFW via MBT

Worker Answer; Administrator Reply (sender end)

Master/Read		from Mbus devices (32 bit address)

Admin get L2 Answer (from MBT)

Slave devices:  processor-programmable 1MB window: Mbus address space to memory

Slave/Write		by other Mbus device (e.g. another alpha writes to my mailbox)

Worker Answer; Administrator Reply (mailbox end)

Slave/Read		by other Mbus device (e.g. it reads back of my mailbox for checking)